## Slide 1: Intermediate thesis presentation
Optimal operation of CHP’s under uncertainty – Jef Daniëls
Promotor: Pr. Dr. Ir. W. D’haeselaer
Assistant: Juliana Zapata Riveros

## Slide 2: Overview
Introduction
Goal
Research questions
Methodology
Semester planning

## Slide 3: Introduction – CHP
Combined Heat & Power
Micro-CHP < 50 kW
Technologies
  Stirling
  Fuel cell
Fuel
Power plant
Electricity
Fuel
Boiler
Heat
CHP
Electricity
Heat
55%
98%
40%
56%
56%
44%
100%
Overall efficiency: 74%
Overall efficiency: 96%
Separate generation
cogeneration
Notes: CHP: generates simultaneous heat and power -> better overall efficiencies than separate power production

## Slide 4: Introduction – Fuel cells
 |  |  | Heat engines |  |  | Fuel cells |  |  |  |  | 
1kW-50kW |  |  | ICE | Turbine | Stirling | PEMFC | AFC | PAFC | MCFC | SOFC | DMFC
Power range [kW] |  |  | 1-50 | 10-50 | 1-50 | 1-50 | 10-50 | >50 | >50 | 1-50 | 1-50
Efficiency [%] |  |  |  |  |  |  |  |  |  |  | 
 | Electrical 100% load |  | 20-30 | 20-25 | 15-30 | 45 | 50 | 40 | >50 | >50 | 40
 | Electrical 50% load |  | 15-20 | 17-22,5 | 15-30 | 45 | 50 | 40 | 50 | 50 | 40
 | Overall |  | 85-90 | 80-90 | 80-95 | 95 | 80-90 | 80-90 | 80-90 | 95 | 80-90
Capital costs [$/kW] |  |  | 1000-2500 | 1500-2500 | 5000 | <1500 | 1800 | 2100 | 2000-3000 | 3000 | -
Proven track record – Ene-farm Japan
~50 000h; >20 000 units
Fuel cells promise the highest efficiency compared to other micro-CHP’s
Notes: CHP: generates simultaneous heat and power -> better overall efficiencies than separate power production

## Slide 5: Introduction – Wind uncertainty
Others
  Electricity, heat
  Wind, solar
Forecasts reduce uncertainty, but errors remain
How can we reduce this error uncertainty?

## Slide 6: Goal
Optimal operation of CHP’s under uncertainty
  Focus on residential and tertiary fuel cell cogeneration
  Focus on wind energy
  Virtual Power Plant
Reduce wind forecast error uncertainty with CHP’s

## Slide 7: Goal – VPP
Aggregator
  Wind turbines
  Distributed cogeneration (CHP’s)
  (Heat pumps)
Reduce uncertainty by aggregating CHP’s and wind turbines
Notes: CHP: generates simultaneous heat and power -> better overall efficiencies than separate power production

## Slide 8: Goal – Literature
Papers about cost reduction
  Lack investment cost
  Other way round
Almost no papers about CHP’s to compensate wind error
No papers compare CHP with other techniques (type of uncertainty)
Notes: CHP: generates simultaneous heat and power -> better overall efficiencies than separate power production

## Slide 9: Research questions
What is the cost/type of uncertainty?
Amount of units necessary to reduce this cost?
Profitable investment cost/unit?

## Slide 10: Methodology – Uncertainty
Notes: We make a bidding, then operate the CHP’s in such a manner that heat demand is met and the imbalance is reduced as much as possible

## Slide 11: Methodology – Deterministic model

## Slide 12: Methodology – Equations
Maximise investment cost (=objective)
Notes: E = startup cost

## Slide 13: Methodology – Equations
Grid
Reduction of imbalance
Notes: E = startup cost

## Slide 14: Methodology – Stochastic model
Different error scenario’s
  Scenario generation via historical data
  Scenario reduction and probabilities
Optimal number of CHP’s required

## Slide 15: Methodology – Data
Aggregated Belgian data
  750MW
  Simulate 1MW wind turbine
Order of 10-20kW CHP units
  To make results computable

## Slide 16: Methodology – Case studies
CHP + boiler (+ battery)  base case
Heat pump + boiler + battery
CHP + heat pump + battery
Decide how many CHP’s required to make minimal investment cost

## Slide 17: Semester planning
Deterministic model (end of January)
Stochastic model (end of March)
  Scenario generation
  Scenario reduction
Developing other case studies (April)
Writing (April)

## Slide 18: Goal
Analyse the cost and behaviour of wind uncertainty and the corresponding profitable investment cost for CHP’s and heat pumps

## Slide 19: Methodology – Equations
Heat demand = HD
Heat supply = HS
Fuel supply = FS
Elec. Supply = ES
Time = set i
Houses = set j

## Slide 20: Methodology – Equations
Maximise investment cost (=objective)
Notes: E = startup cost

## Slide 21: Methodology – Equations
Grid
Reduction of imbalance
Notes: E = startup cost

## Slide 22: Methodology – Equations
Heat demand
Storage
CHP
On/off

## Slide 23: Methodology – Equations
Boiler
HP